## Slide 1: SYSTEMS FOR AUTONOMOUS AIRCRAFT FINAL PROJECT 2025-2026
PROJECT GUIDE: Prof. ROBERTO OPROMOLLA
CAMERA CALIBRATION

## Slide 2: Camera Specs which camera?
Sensor Resolution: 50 MP
Aperture: f/1.4.
Sensor Size: 1/1.55“
Pixel Size: 1.0µm (2.0µm with Quad Pixel Technology)
Focal Length: 25mm (35mm equivalent)
Focus Technology: Multi-directional PDAF (Phase Detection Auto Focus) + Laser AF
Stabilization: OIS (Optical Image Stabilization)
Color Validation: Pantone™ Validated (True-to-life color and skin tone accuracy)

## Slide 3
Test four distortion models:
1. 4th order radial only (k1, k2)
2. 4th order radial + tangential (k1,k2,p1,p2)
3. 6th order radial + tangential (k1,k2,k3,p1,p2)
4. Full model with skew (k1,k2,k3,p1,p2,α)
Analyze:
Effect of image count on calibration quality
Optimal model selection using score metric
Score Metric (details on Slide 18): Combines parameter uncertainty + reprojection error → Lower score = better calibration
PROBLEM STATEMENT
- For each model, report:
Intrinsic parameters + uncertainties (σ)
Extrinsic parameters (R, t for each image)
Reprojection errors (per image + mean)

## Slide 4
INTRODUCTION
A planar checkerboard with known square size is used. For each image, the corner points are detected in the image and associated with known 3D coordinates in the checkerboard reference frame.
The calibration problem is solved by minimizing the reprojection error using nonlinear least squares.
A checkerboard with square size 25 mm was used.
A total of 21 usable images were acquired with different orientations and positions.

## Slide 5
METHODOLOGY
Pinhole Camera Model
  Ideal projection: x = X/Z , y = Y/Z
  Pixel coordinates: u = fx x + cx , v = fy y + cy.
  Homogeneous form: [u v 1]^T = K [R | t] [X Y Z 1]^T
  Intrinsic matrix K: fx, fy, cx, cy, skew
Distortion
  Radial Distortion Model (Plumb-Bob)
  Let the normalized image coordinates be :
)
Interpretation
are radial distortion coefficients
Distortion:
  Is zero at the image center
  Increases towards image borders
Models:
  Barrel distortion (lines bend outward)
  Pincushion distortion (lines bend inward

## Slide 6
METHODOLOGY
Distortion
  Radial Distortion Model (Plumb-Bob)
  Let the normalized image coordinates be :
:
p1​,p2 ​ = tangential distortion coefficients
Distortion is usually much smaller than radial distortion
Depends on lens alignment, not lens shape
SKEW
  Skew represents non-orthogonality between the image x and y axes
  It appears when:
    Pixels are not perfectly rectangular
    The sensor axes are not exactly perpendicular

## Slide 7
CALIBRATION
4th order radial, no tangential, no skew
Intrinsic Calibration Results
  Estimated Parameters
    Focal length:
    px, px
    Principal point:
    px, px
    Radial distortion:
    ,
Uncertainties (Standard Deviations)
  Focal length uncertainty:
  px, px ~0.4% relative error
  Principal point uncertainty:
  px, px
  Radial distortion uncertainty:
  ,

## Slide 8
Parameter | Value | σ | σ/val
fx (px) | 3019 | 11.6 | 0.4%
fy (px) | 3007 | 11.7 | 0.4%
cx (px) | 2033 | 6.9 | 0.3%
cy (px) | 1558 | 4.8 | 0.3%
k1 | 0.1556 | 0.0098 | 6.3%
k2 | -0.6846 | 0.0453 | 6.6%

## Slide 9
CALIBRATION
4th order radial, no tangential, no skew
Mean error: 1.51 px (RMS over all corners, all images)
Per-image distribution:
Best: 0.26 px (sharp, well-lit, frontal view)
Worst: 3.65 px (blur, extreme angle, or occlusion)

## Slide 10: CALIBRATION
Interpretation
Calibration is globally consistent
A few low-quality images dominate the mean error
No catastrophic outliers → dataset is stable
So, Accuracy is acceptable but limited by:
  Image quality
  Symmetric checker board
  Corner detection accuracy
Error Range | #Images | %
< 1.0 px | 8 | 38%
1.0-2.0 px | 9 | 43%
2.0-3.0 px | 3 | 14%
> 3.0 px | 1 | 5%

## Slide 11
CALIBRATION
4th order radial, no tangential, no skew
Extrinsic Parameters
Camera poses cover:
    Different distances (Z direction)
    Different orientations (tilted views)
    Different lateral positions (X, Y)
This geometric diversity is essential for good calibration
Interpretation
The wide spread of poses:
    Improves parameter observability
    Reduces parameter correlation
No degenerate configuration:
    No all images from same position
    No all images fronto-parallel

## Slide 12
CALIBRATION
4th order radial, tangential, no skew
Intrinsic Calibration Results
  Estimated Parameters
    Focal length:
    px, px
    Principal point:
  px, px
    Radial distortion:
    ,
    Tangential distortion:
  ,
Uncertainties (Standard Deviations)
  Focal length uncertainty:
  px, px ~0.4% relative error
  Principal point uncertainty:
  px, px
  Radial distortion uncertainty:
  , 7
  Tangential distortion uncertainty:
Interpretation
Focal length and principal point are well estimated and stable
Radial distortion coefficients are well constrained
Tangential distortion: Small magnitude
Uncertainty is of the same order → weakly observable
Overall calibration is numerically stable

## Slide 13: Comparison: Model 1 vs Model 2
Parameter | Model 1 | Model 2 | Δ Change
cx (px) | 2033 | 2066 | +33 px
cy (px) | 1558 | 1574 | +16 px
k1 | 0.1556 | 0.1523 | -2.1%
k2 | -0.6846 | -0.6711 | -2.0%
σ_cx (px) | 6.9 | 8.8 | +27%
Interpretation
Tangential terms slightly alter distortion model
Uncertainties increase (decorrelation) → GOOD
Mean error unchanged (1.51 px) → No improvement

## Slide 14
CALIBRATION
4th order radial, tangential, no skew
Intrinsic Calibration Results
  Reprojection error is not uniform across images
  Some images show large errors (~3–3.6 px):Likely due to blur, poor lighting, or extreme perspective
  Many images show small errors (< 1 px):Good quality and well-conditioned views
  Final mean reprojection error ≈ 1.5 pixels
Interpretation
Calibration is globally consistent
A few low-quality images dominate the mean error
No catastrophic outliers → dataset is stable

## Slide 15
CALIBRATION
4th order radial, tangential, no skew
Extrinsic Parameters
Camera poses cover:
    Different distances (Z direction)
    Different orientations (tilted views)
    Different lateral positions (X, Y)
This geometric diversity is essential for good calibration
Interpretation
The wide spread of poses:
    Improves parameter observability
    Reduces parameter correlation
No degenerate configuration:
    No all images from same position
    No all images fronto-parallel

## Slide 16
CALIBRATION
6th order radial, tangential, no skew
Intrinsic Calibration Results
  Estimated Parameters
    Focal length:
    px, px
    Principal point:
  px, px
    Radial distortion:
    ,
    Tangential distortion:
Uncertainties (Standard Deviations)
  Focal length uncertainty:
  px, px ~0.4% relative error
  Principal point uncertainty:
  px, px
  Radial distortion uncertainty:
  ,
  Tangential distortion uncertainty:
Interpretation
Focal length and principal point are stable
But: 𝑘_2and 𝑘_3 have huge uncertainties
𝑘_3=−0.95±0.74 This means,
  The parameter is poorly observable
  This is a clear sign of overfitting
Tangential distortion is weakly observable
This model is over-parameterized

## Slide 17
CALIBRATION
6th order radial, tangential, no skew
  Reprojection error distribution is very similar to simpler models:
  Some images: ~3–3.6 px
  Many images: < 1 px
  Global mean error is almost identical to:
    4th-noT-no
    S4th-T-noS
Interpretation
Despite more parameters (k₁, k₂, k₃ + p₁, p₂),The reprojection error does not improve

## Slide 18
CALIBRATION
6th order radial, tangential, no skew
Extrinsic Parameters
Camera poses cover:
    Different distances (Z direction)
    Different orientations (tilted views)
    Different lateral positions (X, Y)
This geometric diversity is essential for good calibration
Interpretation
Good geometric diversity is present:
  This is necessary for reliable calibration
The pose distribution is very similar to the simpler models:
  The complex distortion model does not change camera geometry

## Slide 19
CALIBRATION
6th order radial, tangential, skew
Intrinsic Calibration Results
  Estimated Parameters
    Focal length:
    px, px
    Principal point:
  px, px
    Radial distortion:
    ,
    Tangential distortion:
  ,
    Skew:
Interpretation
  Skew:
      No improvement in reprojection error
    Much worse parameter uncertainties
    Physically meaningless parameters
    Clear evidence of overfitting
Uncertainties (Standard Deviations)
  Focal length uncertainty:
  px, px ~0.4% relative error
  Principal point uncertainty:
  px, px
  Radial distortion uncertainty:
  ,
  Tangential distortion uncertainty:
  Skew:

## Slide 20
CALIBRATION
6th order radial, tangential, skew
Intrinsic Calibration Results
  Reprojection error is not uniform across images
  Some images show large errors (~3–3.6 px):Likely due to blur, poor lighting, or extreme perspective
  Many images show small errors (< 1 px):Good quality and well-conditioned views
  Final mean reprojection error ≈ 1.5 pixels
Interpretation
Despite3 radial coefficients, Tangential distortion, Skew the reprojection error does not improve at all

## Slide 21
IMAGE COUNT ANALYSIS
Number of Images | Mean Reprojection Error | σ_fx (px) | Selection Strategy
3 | 2.45 px | 18.2 | Diverse pose
5 | 2.74 px | 15.6 | Random
7 | 2.84 px | 14.1 | Random
10 | 2.49 px | 13.3 | Random
21 | 1.51 px | 11.6 | All images
Error does NOT decrease monotonically
Image QUALITY matters more than QUANTITY
Uncertainty (σ_fx) DOES decrease monotonically
More images = more stable estimation

## Slide 22: IMAGE COUNT ANALYSIS
With few images:
  Poor geometric coverage
  Poor parameter observability
  Large reprojection error
As number of images increases:
  Viewpoint diversity increases
  Estimation becomes more stable
  Error decreases significantly
CONCLUSION:
- Minimum: ~10 images for stable calibration
Optimal: 20-30 high-quality, diverse images
Adding poor images can HURT accuracy!

## Slide 23
SCORE METRIC
Where:
= standard deviation (uncertainty)
= estimated parameters
= reprojection error components
The score measures:
  Relative uncertainty of parameters
  Plus geometric reprojection accuracy
Lower score means More accurate More stable More reliable

## Slide 24
SCORE METRIC
Performance Score Comparison Between Models
Model | Omnivision 50 MP Score | Samsung 12MP Score
4th-noT-noS | 1.65 | 1.38
4th-T-noS | 1.66 | 2.21
6th-T-noS | 3.11 | 2.95
6th-T-S | `3.51 | 3.55
CONCLUSION: The 4th-noT-noS model is the best compromise between accuracy and stability.

## Slide 25
THANK YOU